## Slide 1: General
Format square (fit to Eckelmann window)

## Slide 2: Manual Mode: Height Adjustment
10mm
It is the height from the
cutting table for preheat, piercing etc.
When pressing the button,
torch will move to that height
Height can be adjusted with Up Down?

## Slide 3: Process Mode: Process is off
Height/Man
When process is off, switch between
Manual control and Height sensor control
8mm
Preheat Height (handling as with existing SW)
8mm

## Slide 4: Process Mode: Process is active
When process is on, switch between
Height control on and off

## Slide 5: Process mode: Process is active
50000 | 6mm | PSF3-6
405mm/min 1,6 mm kerf
Preheat
30
Actual pressure or flow value
Current data set loaded to CU+
Current process status
Off, preheat, pierce, cut
Current status message (latest error etc.)
Touching field open error list (all stations)
Flame(H-O): 1,5 1,7
Flame(F-G): 0,2 0,2
When preheating is active, Menue and error list
can not be opened or will be closed

## Slide 6: Group: Torch Parameter
Ignition detection enable/disable Level 1
Flashback sensitivity Level 1
Flame offset Level 1

## Slide 7: Gas
Gas -> Menue name
Lock Gas Flow -> Sub Menue name
  Pressure output Lock/Unlock Level 1 -> Parameter
Pressure Test -> Sub Menue name
H-O Slider Enable/Disable
C-O Slider Enable/Disable
F-G Slider Enable/Disable

## Slide 8: Service
Help button Level 0 – 2 (based on login level)
System log (Cu+ Histogram PLISTorch Histogram) FOR ALL STATIONS Level 1